Changzhou RATTM MOTOR Co.,Ltd

Catalog

1. Product overview............................................................................................ 2

2. Product appearance figure............................................................................ 2

3. Product characteristic curve graph.............................................................. 3

4. Product technical parameter table................................................................ 4

5. Spindle installation explanation................................................................ 5~8

1) Circulation cooling system instructions......................................................... 5

- Air seal (AS) ................................................................................................. 5

- Compressed gas air quality requirements .................................................... 5

- Running-in program instructions .................................................................. 5

- Product backend interface explanation ...….................................................. 5

- Product locking and unlocking tool signal instructions ................................. 6

- Thermistor parameters ..…........................................................................ 7-8

- Product rear end gas line explanation........................................................... 8

6. Products using precautions…………............................................................. 9

1) Product installed process precautions........................................................... 9

- Maintain maintenance precautions……........................................................ 9

7. Product common malfunctions&method of exclusion………...………….. 10

1. Product overview

1) This spindle is built-in type spindle motor, built-in three asynchronous motors,by the inverter control.As the spindle has a compact structure,high power, big torque, small vibration, low noise characteristics,so it can achieve high speed,high powe cutting,high precision and high stability operation.

2) The bearing of spindle use grease lubricated angular to contact bearings,can be achieved lifelong lubricating within the life cycle.

3) The spindle use forced coolling mode to coolling motor,front and rear bearings.Coolant flow through the reasonable arrangement cycle watercourse of the spindle body,thus can take the heat generated of the spindle rotation speed, to achieve thermal equilibrium,let spindle temperature within a certain constant value. External cooling device effect:maintaining a constant temperature of the coolant.

4) The spindle built-in PTC 140 temperature sensor(Technical parameters are visible in other sections of this specification),you can read it anytime if you need to protect the motor temperature.

5) The tool clamping methods:this spindle built-in automatic tool change device,shank form is BT30.

2. Product appearance figure

3. Product characteristic curve graph

Voltage--speed (frequency) curve graph

Power--speed (frequency) curve graph

Torque-- speed (frequency) curve graph

4. Product technical parameter table

| Spindle model: | RTM120x103-30-24Z/4.5 220V | Voltage: | 220V |
| --- | --- | --- | --- |
| Maximum speed: | 24000rpm | Rated frequency: | 800Hz |
| Electric current: | 15A | Motor pole: | 4P |
| Rated power: | 4.5KW (S1) | Peak power: | 5.4KW (S6) |
| Rated torque: | 3.5Nm | Peak torque: | 4.2Nm |

| Technical parameters |
| --- |
| No. | Project | Standard |
| 1 | Spindle blowing dust/seal gas pressure (MPa) | 0.2-0.25 |
| 2 | Spindle gas seal gas flow (L/min) | 65±10 (When on Working) |
| 3 | Cooling water pressure (MPa) | ≧0.25 |
| 4 | Cooling water flow (L/min) | ≧2.5 |
| 5 | Cooling water temperature(℃) | 24-28 |
| 6 | Spindle static state pulse (µm) | ≦3 |
| 7 | Spindle vibration (mm/s) | ≦1.0 |
| 8 | Spindle assembly method | Bottom mounting(6-M8) |
| 9 | Motor windings Pressure test (V/M) | 1000V/1 minute withstanding Voltage test |
| 10 | Tool Interface | BT30 |
| 11 | Inverter Specifications | 5.5KW (220V) |
| 12 | Fitment | Woodworking machinery, polishing industry, etc. |

- Spindle installation explanation

- Fan cooling system description

When the spindle rotates, the rear fan system must be started to ensure the correct supply voltage and the supply voltage is 12V.

- Air sealing control (AS)

In order to prevent water or impurities enters internal of the spindle,spindle will have gas sealing device,the gas seal machine must be started start with the machine at the same time. And the need to go through multi-stage filtration.

- Compressed gas quality requirements

The quality requirement of gas which is used in gas seals:

Oil content: ﹤0.01mg/m³

Solid particle: ﹤5µ m

Pressure dew point: ﹤7.5℃(0.7MPa)

4) Running-in program instructions

Only all monitoring issued no failures operational signals,at the same time,all safety devices have been installed and working properly,then allow start spindle.

Note: new or spindle which is not used for a long time must to be running slowly.First,start run spindle for half an hour as 25% of the maximum speed,then increase to 50% of the maximum speed,to run 15 minutes,finally, increase to maximum speed.It’s need to check the temperature of the spindle during the whole process, spindle will get hot, but not hot hand, if the spindle becomes hot, pls stop the operation and contact our customer service department.

5) Product backend interface instructions

| No. | Function | Definition |
| --- | --- | --- |
| 1 | Gas sealing (Protection of impurities into the spindle 0.2-0.25MPa) | Ф6 |
| 2 | Return air (piston reset 0.35-0.45MPa) | Ф6 |
| 5 | Power supply (Spindle power lines with thermistor) | U/V/W/ Ground wire |
| 6 | Intake air (Spindle loose knife 0.5-0.6MPa) | Ф6 |
| 7 | Sensor (spindle tool change signals 24V) | Broach / loose knife |
| 8 | Fan (spindle cooling) | 12V |

6) PTC140 Temperature coefficient thermistor parameters

Our products are equipped with a single thermistor PTC140, it can be used for spindle temperature protection.

| Parameter name | Parameter symbol | Single core | Three core Series connection | Unit |
| --- | --- | --- | --- | --- |
| Maximum DC working temperature | Umax | 30 | 30 | V |
| Rated control temperature | Tk | Designed according to user | ℃ |
| Rated control temperature tolerance | T1 | ±5℃ | ±5℃ | ℃ |
| Rated control temperature tolerance | T2 | ±0.5℃ | ±0.5℃ | ℃ |
| Resistance value on 25℃ | R25 | ≤100 | ≤300 | Ω |
| Rated control temperature on -5℃ resistance value | Tk-5℃ | ≤550 | ≤1600 | Ω |
| Rated control temperature on +5℃ resistance value | Tk+5℃ | ≥1330 | ≥4000 | Ω |
| Rated control temperature on +15℃ resistance value | Tk+15℃ | ≥4 | ≥12 | KΩ |
| Thermal response time | Ta | ≤5 | ≤5 | S |
| Dielectric strength | Uis | AC2.5 | AC2.5 | KV |
| Maximum control temperature | Tkmax | 180 | 180 | ℃ |
| Maximum allowable storage temperature | Tmax | 180 | 180 | ℃ |
| Minimum allowable storage temperature | Tmin | -40 | -40 | ℃ |

7) Product Tool Change Signals Description

Sensor Model (0-24V, PNP), The spindle built two sensors.wiring Diagram is as follows:

1. Response broach knife signal, when the knife handle is hang, black sensor output signal;

2. Response loose knife signal, when the knife jaws open,black sensor output signal;

8) Product backend pneumatic description

--A、B (Two position five port changeover valve) change-over valve

A→intake air(0.5-0.6MPa)

B→Quick exhaust value →return air

Total air intake→one-way valve→ pressure gauge→filter

--Adjustable One-way valve→air seal(0.2-0.25MPa)

- Wiring definition

Power supply, Fhermal, Fan

Thermal: 1, 5

Fan: 3 Black,9 Red

Power supply: 4 Red U,6 Black V,8 Blue W

Ground: 2 Yellow,Green

Proximity switch and push button switch

Proximity switch                                       Switch button

Hanging knife: 1                                                 5 Red

Unloading knife: 2                                              11 Red

0V: 6 Blue                                                       7 Blue

24V: Brown                                                    8 Blue

6. The usages of the product and warnings

Matters need attention when you install this spindle

1) Before installed,please read this manual carefully,then operate this sapindle according to instructions requirements specification;

2) When installed, please carefully, pay attention to personal safety and to avoid injuries occurred during the installed process;

3) Suggest tool used by spindle compliance with IOS1940 specifications dynamic balance level within G1.0.

4) Do not use any tools tapping spindle;

5) Do not use sandpaper and grinding wheel to wipe or grind in axis core and taper hole;

6) Use special removal tool to remov the lock nut and the tool;

7) Untrained personnel can not disassemble and operate electric spindle;

Attention to maintenance and maintenance

1) Electric spindle storage temperature is 20 ℃ ± 10 ℃, humidity ≦ 85%, to allow time to store up to three months;

2) Electric spindle most suitable ambient temperature is 20 ℃ ± 10 ℃, bearing life can achieve the desired optimum value;

3) The power cord must take waterproof measure, electric spindle housing must be grounded;

4) Electro-spindle must not exceed nameplate parameters;

5) When electric spindle stop, should cut off the power, it must maintain a certain time after spindle completely stopped to wait spindle heat dissipation, then cut off the coolant, If you disable a long time, you need use compressed air,to remove the residual coolant liquid in the cooling pipe.

6) Not allowed to use any mechanical way to forced braking in the shaft;

7) After using the spindle every day,you should wipe spindle taper,then smear with rust oil;

8) Workplace must be clean, there should be strict dust control measures to prevent foreign matter enter the spindle.

7. Product common malfunctions&method of exclusion

| Fault phenomenon | Reason | Method of exclusion |
| --- | --- | --- |
| Electric spindle is not running after boot | 1. No inverter power output or set incorrectly | Check that VFD supply three-phase output voltage and setting method |
|  | 2. Spindle plug is not inserted | Check the electrical spindle plug and connection. |
|  | 3. Bad plug connector |  |
|  | 4. Bad stator line package | Replace line package |
| Shutdown after a few seconds of the boot | 1. Electric spindle feed water bad insulation line package | Drying line package |
|  | 2. Electric spindle high temperature cause line package insulation damaged | Replace line package |
|  | 3. Electric spindle lose phase to run,then cause overcurrent protection blackout | Check the electric spindle connection |
|  | 4. Start time is too short | Increase the acceleration time |
| Electric spindle smoking or the housing hot after a few second of the boot | 1. Inverter output voltage, frequency are not match the use of electric spindle voltage and frequency | Check the VFD and the spindle voltage, frequency |
|  | 2. The VFD is not set correctly | Reset the VFD |
| Locking nut loose when it is started | Wrong direction of rotation | Change the direction of rotation |
| Spindle have big noise and vibration | 1. Bearing wear seriously | Replace the bearing |
|  | 2. Precision of parts damaged,it’s effect dynamic balance | Calibration of dynamic balance |
|  | 3. Big beat of Spindle | Replace the spindle |
| Locking nut loose when it is stoped | Stop time is too short | Increase the deceleration time |

# Text boxes

Automatic tool changing machining center electric spindle

RTM120x103-30-24Z/4.5 220V

User Instructions